## Slide 1: Ferry Safety in Indonesia October 2019
Elena Chesheva Transport Cluster Leader for Indonesia and Timor-Leste

## Slide 2: 2017 INDONESIA FERRY TRANSPORT DEVELOPMENT
No Ferry lane 278 :
55 Commercial
223 Pioneer
446 Ferry Ports
289 unit Commercial
91 unit Pioneer
380 Unit vessels
Kapal penyeberagan perintis
Kapal penyeberangan komersil
Information from National Transportation Safety Commission

## Slide 3: Indonesia: number of accidents and fatalities 2000 - 2019
  Since the year 2000 there were 2945 fatalities

## Slide 4: Fatal Accident on Lake Toba – June 2018
  167 people died, 19 were rescued
  Ferry was 4 times overloaded (designed for 48 passengers) plus 70 motorcycles (not allowed for by the design)
  Illegal vessel modification
  Stability issue
  Obstructed egress
  Unavailable safety equipment
  Bad weather
  No proper communications system
  Inadequate search and rescue
  In Lake Toba more than 300 ferries operate, but only 4 are certified
  35 landings, inefficient use of constructed terminals

## Slide 5: Lake Toba Visit together with WFSA

## Slide 6: Ferry Safety Challenges – nation-wide
  No system of advance booking, no electronic ticketing in majority of operations
  Ineffective passenger and cargo manifest system, no enforcement of loading limits, control of passengers
  Operational Issues: vehicle’s cargo handling and securing, vehicle stowage, inaccurate or absence of stability calculation, no weight information
Unreported and uninspected cargo inside vehicles: hazardous cargo – (fire hazards for RoRos)

## Slide 7: Ferry Safety Challenges – nation-wide
Ship design not appropriate for designated area of operation, substandard, vessel alterations
Weak seamanship practice
Ferry traffic monitoring, communications systems inefficient
Risk assessment during heavy weather, weather monitoring
Shortcoming of Safety and Emergency Equipment
Crew preparedness and training

## Slide 8: Recommendations

## Slide 9: Recommendations - Operations
Create master plan for Lake Toba ferry operations – terminals, vessels, routes.
Cargo monitoring and passenger embarkation process: improving cargo and passenger reporting system
Control the number of passengers and cargo to regulated levels - manifests
Establish communication systems for ferries - VHF radio for lake Toba ferries
Weather detection and communication - expand Automatic Weather Monitoring Display system piloted in Tiga Ras and establish weather monitors at the major terminals
Plan services during peak tourist activity (esp during Ramadan)

## Slide 10: Recommendations
Crew Competence
  Mandate competence for skippers (captains) and crew
  Improve crew readiness and performance to handle the emergency situation – drills, training
  basic International Convention for Safety of Life at Sea (SOLAS) training for all crew plus advanced training for certain functions
Safety equipment and its proper storage – availability
Effective and availability SAR Response

## Slide 11: Recommendations
Improve Vessel safety:
Register and certify vessels
Phase out substandard vessels
Start developing new safer and cleaner vessels
Regulatory aspect and governance:
National level work on regulatory framework, standards, SOPs and guidelines
Clear division of responsibilities

## Slide 12: World Bank Support

## Slide 13: World Bank Engagement
Policy dialogue and expert advice
Tourism project – investments in Lake Toba facilities,
  Lake Toba Transport Safety improvement proposal as part of Integrated Tourism Masterplan
Potential Ports Projects in Maluku and Nusa Tenggara Timur (NTT) provinces – optimization of RoRo services including focus on safety

## Slide 14
Thank you